## Slide 1
04
Comprehensive Utilization of Sweet Potato by-products

## Slide 2
Approximately 10 to 20 tonnes of waste water and 4.5 to 5.0 tonnes of fresh residues are generated from 1 tonne of starch production.
The production of sweet potato leaves was equivalent to that of roots.
Most waste water and leaves is discharged directly;
About 20% of the residues are used as low-value animal feed; about 80% of the residues are disposed;
A major contributor to serious resource waste and environmental pollution.

## Slide 3
Processing technology of sweet potato protein
Processing technology of native sweet potato protein
Waste water
Concentration
Adjusting pH to 4 with HCl and stirring extraction
Centrifugation and collecting precipitate
Adjusting pH to 8 with NaOH
Ultrafiltration
Spray drying
Native sweet potato protein

## Slide 4
Waste water
Concentration
Preheating
Heat preservation
Steam ejector
Processing technology of denatured sweet potato protein
Flocculation
Concentration
Spray drying
Protein
Plate-frame pressure
filtration
Wet protein
Airflow drying
Protein

## Slide 5
Processing technology of sweet potato dietary fiber
Sweet potato residues
Enzyme hydrolysis
Turbine centrifuging
Three-column centrifuging
Plate-frame pressure filtration
Drying
Smashing
Superfine grinding
Dietary fiber

## Slide 6
Processing technology of sweet potato pectin
Sweet potato residue
Thermostable α-amylase treatment
Centrifugation
Acid extraction from the precipitate
Crude pectin solution
Ethanol precipitation
(ethanol : crude pectin solution, 4:1, v/v)
Centrifugation and
collecting precipitate
Drying
Pectin

## Slide 7
Processing technology of cellulose nanocrystals from sweet potato residues
Purple sweet potato peel residues after anthocyanin extraction
Weigh 10 g
Add 25 mL 5%(w/w) α-amylase solution and 250 mL deionized water, 95℃ for 3 h
Add 200 mL of sodium chloride (10 g/L), 70℃ for 2 h
Repeat this step for 2-4 times
Add 200 mL of 10 wt.% sodium hydroxide solution, 60℃ for 4 h
Washing residues with distilled water to neutral pH
Washing residues with distilled water to neutral pH
The remained solid was lyophilized for 3 d to obtain cellulose
Washing Filter
Ultrasonic assisted hydrolysis of cellulose by maleic acid to prepare CNCs
[the ratio between cellulose and 75 wt% maleic acid was 1:10 (g/mL), ultrasonic at 60℃ for 1 h, followed by 120℃ for 2.5 h]
CNCs

## Slide 8
Processing technology of sweet potato leaf powder
Fresh sweet potato leaves
Washing
Cutting
Dewatering
Drying
Grinding
Sweet potato leaf powder
Blanching with hot water (80-100 ℃, 1-3 min ) or steaming (90-100 ℃, 2-3 min)

## Slide 9
Processing technology of sweet potato leaf polyphenols
Fresh sweet potato leaves
Washing
Cutting
Extraction and purification
Drying
Sweet potato leaf polyphenols
Fresh sweet potato leaves
Washing
Cutting
Extraction and purification
Drying
Sweet potato leaf polyphenols

## Slide 10
Thank You
Sharing for Learning
The SSTC project is funded by: Ministry of Agriculture and Rural Affairs P. R. China