## Slide 1: Research Progress on Identification and Control Technology of Stored Grain Pests
Prof. WU Yi
Research Field: Stored-grain pests integrated control
Sep 2024

## Slide 2
Stored grain pest identification technology
01
Stored grain pest control technology in China
02
Demonstration of integrated control technology application of new green grain storage technology
03
Research progress on identification and control technology
of stored grain pests

## Slide 3
Pests
Upgrading of storage facilities, technological development, climate environment, and changes in the occurrence and development of stored grain pests, including macro level distribution, growth and development, as well as micro level information changes.
Pest control, chemical agent support, low-temperature grain storage pest control; Targeted prevention and control techniques and strategies for pest ecological regions.
Quick and accurate identification - identification of basic databases and systems;
Physical and biological control technologies - protective agents, natural enemy biocontrol.
Issues
needs
Technology needs of stored grain pest control

## Slide 4
Stored grain pest identification technology
01

## Slide 5
Issues：
Identification of the basics of control. Regarding the accurate and rapid identification of pests in stored grain, as well as the weak molecular basic data and mechanisms in prevention and control technology.
Contents：
Establish molecular identification and analysis techniques for insects and mites in stored grain, as well as related databases: three major technical systems and related databases, including DNA barcode molecular identification, 3D recognition, and mitochondrial genome.
To provide technical and basic data support for the classification, identification, and systematic relationship research of stored grain insects and mites, and to serve the monitoring, identification, and pest control of stored grain insects and mites.
Services：
The importance of pest identification

## Slide 6
Achievement 1: Grain Pests DNA Barcode Identification System
Formed the "Certificate Specimen - Morphological Identification - Molecular Barcode -3D Digital Specimen" for grain storage insects and mites
morphological identification
DNA barcode gene identification
DNA barcode sequecing
Construction of DNA barcode library for insects and mites
Validity analysis of DNA barcode identification
PCR amplification and screening of 3 genes: COI, ITS, 18S rDNA, targeting 8 different stored grain pests
At least 5 samples of each stored grain insect should be tested and sequenced bidirectionally to obtain their barcode sequence
(1) Standard COI barcode sequence(2) The sequence length is not less than 600bp(3) No missing bases, no terminators(4) The maximum genetic distance within a species is greater than the minimum genetic distance between species.
Phylogenetic analysis
Evolutionary analysis of haplotype network
DNA barcode sequence library：
Based on the sequence of COI gene，established “Grain Pests DNA Barcode Identification System”，including 50 species insects/mites. DNA barcode can effectively identify the main stored grain insects and mites.
Morphological characteristics
Barcode Research

## Slide 7
Achievement 1: A identification system for stored grain insects and mites, “specimens—morphological identification—molecular barcode identification“
Three types of information databases:
Form display sample
Molecular Information Database
DNA Genome Database

## Slide 8
Achievement 1: DNA barcode of stored grain pests-specific primers identification technology for close species
Analyze nucleotide sequence specific sites of 18 species and design specific primers for close species to complete identification within 7 hours without sequencing.
Morphology Identification | Time（d） |  |  | 
 | Cultivate to adults | Slide production and identification | Total | Average
Eggs | 25 | 5 | 30 | 17
Lava | 1-20 | 5 | 5-25 | 
Adults | 0 | 5 | 5 | 
Table Comparison of Morphology and Molecular Identification of Cryptolestes ferrugineus
Molecular Identification | Time（d） |  |  | 
 | DNA extraction | PCR | Sequencing /electrophoresis | Total
DNA barcode | 0.1 | 0.15 | 2.00 | 2.3
specific primers | 0.1 | 0.15 | 0.05 | 0.3

## Slide 9
A three-dimensional digital system for physical specimens of 25 stored grain pests has been established, which has real textures with a resolution of 4K or above, high-definition VR display, and insect specimen display and integration. It can be used for physical specimen replacement, supporting identification, and teaching and training.
Achievement 2： Three dimensional digital specimen system
for stored grain pests

## Slide 10
Achievement 3: Grain Pests Mitichondrion Identification and Analysis System
Enrich the identification genes of Achievement 1, promote basic research on pest control, and enhance the research capability of rapid and accurate identification, genetic difference analysis, and pest tracing of stored grain pests in China based on mitochondrial.
The main functions include information browsing, information querying, and gene sequence alignment and identification.

## Slide 11
1. Service for basic application of pests control
Complementing traditional morphological identification
Revealing the genetic relationships between species
Research on differences in pest resistance and outbreak patterns.
3. Training in China and internation
2. Molecular identification of stored grain pests-identification of fragments and damaged samples
It is used for the identification of non adult and fragmented insect species, and in the quarantine and identification of food and food imports and exports, to serve the quarantine and identification of insects and mites and ensure food security.
Five sessions of “Green Ecological Grain Storage New Technology Training and Seminar" in China
Two sessions of the Asia Cooperation Dialogue (ACD) training courses
Warehouse training of Suzhou Food and strategic reserves Administration
4. Establish insustry standards
Application situation and social benefits

## Slide 12
Stored grain pest control technology in China
02

## Slide 13
Technical Introduction
Physical protection, independent innovation
Meets food grade requirements and is environmentally friendly
Supporting equipment, mechanization, low cost, wide range of scenarios
Standard, "Regulations on Safe Storage of Grain and Oil", Second prize
1. Food grade inert powder technology for controlling stored grain pests

## Slide 14
More than 130 grain depots in 23 provinces - SINOGRAIN and local grain depots
More than 50 processing enterprises - Yihai and COFCO
More than 500 farmers grain storage application
Application
Empty warehouse insecticide, insecticide line, grain pile surface and local insecticide
After the first fumigation of some grain depots, the entire storage period does not require fumigation to meet the basic requirement of insect free grain.
Effect
1.Food grade inert powder technology for controlling stored grain pests

## Slide 15
Scaling up production: breeding high-yield strains and producing 10 tons or more;
Pesticide registration certificate: Obtained the raw material and 0.5% powder;
Technical regulations: industry standards;
Application equipment: Developed automatic application equipment and application robots.
防效成本
First generation equipment (2015)
Second generation equipment (2016)
Automatic spray application by sensing grain flow
Higher automation, stable performance, and large grain flow
Third generation equipment (2018)
2. Application technology of Spinosad
Technical Introduction

## Slide 16
Application of pesticides on the surface of grain silos based on negative pressure ventilation, using robots for surface application;
When entering the warehouse, mix with the grain;
Ten application grain depots have been established in different grain storage ecological zones.
Empty warehouse insecticide, whole warehouse insecticide, surface and local insecticide of grain piles;
Effective protection time of up to 2 years, with no impact on grain quality;
Dose: 1mg/kg.
2. Application technology of Spinosad
Application
Effect

## Slide 17
3. Predatory mite technology for controlling stored grain pests
Natural enemy biocontrol: using mites to control mites, using mites to control insects;
Scale production: standardized and large-scale breeding techniques;
Application technology: deployment technology, forming norms, no need for equipment;
Long term mechanism: New green, environmentally friendly and sustainable governance.
Predator mite feeding platform
Technical Introduction

## Slide 18
The first large-scale research and application in the grain industry;
Select two advantageous natural enemies of mites suitable for grain depots in China;
For the first time, a predatory mite biocontrol technology system has been established.
Technology innovation
Release at temperatures above 15 ℃, establish a population to reduce the eggs and larvae of pests;
High-temperature and high humidity area is the best. 6 demonstration depots and long-term effects;
2-15 pests per day, ¥4 yuan per 10000 mites.
Effect and cost
Collection and screening
Predatory ability
Application
Small and medium scale trial
3. Predatory mite technology for controlling stored grain pests

## Slide 19
It does not contain toxic pesticide groups such as halogens, heterocycles, and benzene rings, and only contains carbon, hydrogen, and oxygen elements. It is an unsaturated fatty acid ester (similar to vegetable oil)
Chemical structure specificity
Juvenile hormones interfere with the molting process, inhibit the transformation of eggs or larvae into adults, and cause the adults to lose their reproductive ability, thereby controlling the growth of pest populations
Unique mechanism
Does not affect specific insect sites, but interferes with normal growth and development processes, poses no resistance risk, and has no reported resistance
Not easy to develop resistance
When exposed to light in the external environment, it decomposes into carbon dioxide and water, with fast degradation and no residue, Harmless to humans and the environment
Ultra safe and environmentally friendly
The target insects are extremely sensitive, and S-cypermethrin can achieve excellent control effects at ultra-low concentrations ranging from one to three parts per million
High activity, ultra-low dosage
S-Methoprene mechanism
S-Methoprene： Special Structure, Unique Mechanism, Low Quantity, High Sensitivity, Green and Safe
4. S-Methoprene control stored grain pest technology

## Slide 20
4. S-Methoprene control stored grain pests technology
No. | Ecological zone | Province | Grain | Test warehouses | Introduction
1 | 7 | Guangdong | Rice | Test 1:Temperature controlled (low temperature) storage+S-Methoprene mixed with whole grain Test 2:Temperature controlled (low temperature) storage+S-Methoprene mixed with surface grain Control: Temperature controlled (low temperature) storage+Conventional pest control methods | Short term testing of insect cages, monitoring of prevention effectiveness, residual and quality determination in test chamber 1, quality determination in control chamber, with an experimental period of 1-2 years.
2 |  | Guangxi | Rice | Test: Conventional storage+S-Methoprene mixed with whole grain Control: Conventional storage+Conventional pest control methods | Short term testing of insect cages, monitoring of prevention effectiveness, with an experimental period of 1-2 years.
3 | 6 | Sichuang | Rice | Test: Temperature controlled (low temperature) storage+S-Methoprene mixed with whole grain Control: Temperature controlled (low temperature) storage+Conventional pest control methods | Same with No.2
4 |  | Yunan | Rice | Same with No.1 | Same with No.2
5 | 5 | Fujian | Rice | Same with No.3 | Same with No.2
6 |  | Jiangsu | Rice | Same with No.1 | Same with No. 1
 |  | Zhejiang | Rice | Same with No.1 | Same with No. 1
7 |  |  |  |  | 
8 | 4 | Henan | Wheat | Same with No.2 | Same with No.2
9 | 2 | Xinjiang | Wheat | Test 1: Conventional storage+S-Methoprene mixed with whole grain Test 2: Conventional storage+S-Methoprene mixed with surface grain Control: Conventional storage+Conventional pest control methods | Same with No.2

## Slide 21
Empty warehouse handling
Using equipment for whole warehouse storage
Effect of pest control in grain storage: S-Methoprene full warehouse application technology can effectively prevent and control common pests in grain warehouses. Surface application can effectively suppress the occurrence of pest populations. During high temperature seasons, local pests may occur and require local or full warehouse treatment.
In terms of maintaining grain quality: S-Methoprene will not cause a deterioration in grain quality.
In terms of economic benefits: some grain depots have seen a ¥ 70 yuan increase in grain prices per ton when grain is released, resulting in an additional profit of over 200,000 yuan for a 3,000ton grain depot.
S-Methoprene agent
4. S-Methoprene control stored grain pests technology

## Slide 22
5. Atmospheric adjustment for insect control : N2
Two types of nitrogen production equipment：At present, there are two mature nitrogen gas controlled grain storage technologies, pressure swing adsorption nitrogen production technology and membrane separation nitrogen production technology, equipment and control systems, which are widely promoted and applied in China.
Three concentrations for controlling：
1. Kill the pests , the concentration is over 98% for more than 30 days；
2. Prevent the pests , the concentration is over 95% for more than 60 days；
3. Atmospheric adjustment grain storage, maintaining a low oxygen state of 90-95% nitrogen concentration for a long time slows down the oxidation of fatty acids
Application scale: The application scale of modified atmosphere grain storage technology in China has reached about 35.9 million tons, with an investment cost of 2.3 yuan/ton of grain.
Pressure Swing Adsorption
Membrane separation
Warehouse covered with film and filled with nitrogen

## Slide 23
5. Atmospheric adjustment for insect control : CO2
The concentration of CO2 for killing the pests
Used to kill various types of pests, the concentration of CO2 in the sealed grain pile should reach 35% or above and be maintained for more than 15 days.
The mode of CO2 adjustment
Fill the tank truck, gasification device, intake circulation pipe of the warehouse, and the grain pile inside the warehouse with bottom filling and top filling.

## Slide 24
6. Fumigation
Fumigant | Characteristic | Note
Phosphine | Highly toxic and safe for pesticide application | 
Sulfuryl fluoride | Poisoning, good spreadability, strong permeability, non corrosive | 
Ozone | Environmentally unfriendly, strong oxidizing agents, and weak penetration power | 
Hydrogen cyanide | Extremely toxic | Prohibited in China
Ethyl formate | Flammable, explosive, not easy to spread in grain piles, easily adsorbed by grain particles | 
Chlorine dioxide (dichloroethane, dichloropropene) | Strong oxidants and expensive gas generation devices | 
Epoxy propane | Flammable, requiring low pressure and oxygen environment | Better fumigation enhancer
Nitric oxide | Unstable, requiring vacuum and ultra-low oxygen environment | 
Ethane nitrile | Flammable, inconvenient to prepare, easily reduced to cyanide, requiring low oxygen environment | 
There are about a dozen fumigation methods for stored pest insecticides that have been studied globally. Phosphine fumigation is widely used in the storage industry, and sulfuryl fluoride has also been applied in recent years.

## Slide 25
Fumigation equipment: pesticide application device; Circulation device; Detection device.
Main influencing factors of fumigation effect
Sealing time: insect species, warehouse airtightness
Drug concentration: design, calculation, detection, temperature
Table 1: Reference Table for Setting Phosphine Concentration during Phosphine Fumigation at Different Sealing Times, Temperatures, and Insect Species.
6. Fumigation: Phosphine

## Slide 26
Demonstration of integrated control technology application of new green grain storage technology
03

## Slide 27
（一） Policy
In June 2021, the Ministry of Finance and Academy of National Food and Strategic Reserves Administration jointly issued document Caijian [2021] No. 177 "Opinions on Deepening the Promotion of High Quality Grain Projects", which proposed "six major improvement actions", including the "Green Warehousing Improvement Action";
In July 2021, the Academy of National Food and Strategic Reserves Administration issued a notice to carry out the pilot work of green grain storage standardization. Actively adopt green grain storage standards, strengthen the application, innovative research and development, and standard revision of green grain storage technology, and explore replicable and promotable typical experiences and working models of green grain storage.
（二）Needs
The industry will comprehensively reduce the use of chemical agents, and “integrated control" will become inevitable;
Continuous investment in scientific research has led to multiple breakthroughs in new green storage technologies in the industry, and the development of a batch of new equipment has made it possible to demonstrate green storage technologies.
Background of Integrated Control Technology Application

## Slide 28
Multi parameter grain monitoring
“early know”
Emergency technology
Integrated control technology system
Optimal Timing
low temperature storage technology
Protective agents: inert powder, Spinosad, S-Methoprene
Natural Enemy Biological Control: Predator Mite Biological Control Technology
Grain conservation and loss reduction
Quality and freshness maintaining
Green storage
Smart storage
target
Green control
Emergency response: Reduction fumigation mainly using aluminum phosphide and sulfuryl fluoride

## Slide 29
Demonstration plan

## Slide 36
Thank You
Sharing for Learning
WU Yi
18811345781 wuyi@ags.ac.cn